## Slide 1
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
AI is reaching operating fleets. Comparable returns remain hard to establish.
196 company-adoption profiles across 93 companies, October 2024–October 2026. Follow deployment, reported results and their original sources. This collection is not an industry census.
Open the interactive report and every original source
01 / 8 OCT 2026
196
company AI projects
across 93 companies
133
described as operating or scaled
54
report a realized (measured) result
32
of those are reported by the operator itself
1
pairs AI investment and
financial benefits:
Ecopetrol’s 2025 portfolio
What it means
1
Artificial lift has detailed fleet evidence.
Devon runs autonomous lift on 1,000 wells, ExxonMobil gas-lift on 1,300+ Permian wells, Chord on ~99% of its rod-lift wells.
2
Pilot uplift does not establish fleet uplift.
Devon’s only uplift figure (2–3%) is from its 2025 pilot; no fleet result is published. Most gains lack a stated baseline.
3
Keep the author and the measurement scope visible.
21 of 54 reported outcomes come from vendor sources. Our bounded search did not verify a named operator cancellation.
Notes: [Sources]
- Energy AI Observatory register - https://energy-ai-observatory-raj.rmistry.chatgpt.site/
- Ecopetrol 2025 sustainability annex (Circular 031), p.209 - https://www.ecopetrol.com.co/wps/wcm/connect/4fec4771-90bd-446d-a107-cbe140583b88/Circular-031-esp-anexo-vf.pdf?CVID=pP5vUHj&MOD=AJPERES
- Devon Energy · Moving beyond pilots - https://s2.q4cdn.com/462548525/files/doc_financials/quarterly/2025/q4/Q4-2025-DVN-Q-A-Webcast-Commentary-Transcript.pdf
- Devon Energy · More than 850 wells live - https://s2.q4cdn.com/462548525/files/doc_financials/quarterly/2026/q1/Q1-2026-DVN-Q-A-Webcast-Commentary-Transcript.pdf
- Devon Energy · 1,000 wells live - https://s2.q4cdn.com/462548525/files/doc_financials/quarterly/2026/q2/Q2-2026-DVN-Q-A-Webcast-Commentary-Transcript.pdf
- Chord Energy · About 99% of rod-lift wells - https://ir.chordenergy.com/2026-02-25-Chord-Energy-Reports-Fourth-Quarter-and-Full-Year-2025-Financial-and-Operating-Results%2C-Issues-2026-Outlook-and-Declares-Base-Dividend
- Chord Energy · Artificial-lift optimization continues - https://ir.chordenergy.com/2026-08-05-Chord-Energy-Reports-Second-Quarter-2026-Financial-and-Operating-Results%2C-Declares-Base-Dividend-and-Updates-2026-Outlook
- ExxonMobil · More than 1,300 Permian wells - https://jpt.spe.org/gas-lift-optimization-in-the-permian-uses-machine-learning-artificial-intelligence-restricted
- ExxonMobil · AI monitors production bottlenecks - https://corporate.exxonmobil.com/locations/india/newsroom/2025/turning-artificial-intelligence-into-business-intelligence
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 2
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
Public evidence: deployment, operating results and financial disclosure
These measures overlap. Some outcomes come from pilots. The 54 result profiles exclude two overlapping portfolio aggregates; stage descriptions come from operator, vendor and secondary sources.
Open the interactive report and every original source
02 / 8 OCT 2026
Chart: 
What the counts mean
Operating status
The other 63 are announcements (29), pilots (27) or unclear (7).
Reported result
56 profiles report a result before overlap exclusions. Another 29 give scale only, 10 a target and 101 no outcome.
Source of the result
32 operator-attributed, 21 vendor-attributed and one independent research result (54 after overlap exclusions).
Financial disclosure
Ecopetrol pairs US$1.88m of AI investment with US$3.50m of benefits in 2025 (revenue +US$2.06m; costs −US$1.44m). Portfolio accounting, not project cash ROI.
Notes: [Sources]
- Energy AI Observatory register (stage and outcome fields) - https://energy-ai-observatory-raj.rmistry.chatgpt.site/#opportunities
- Ecopetrol 2025 sustainability annex (Circular 031), p.209 - https://www.ecopetrol.com.co/wps/wcm/connect/4fec4771-90bd-446d-a107-cbe140583b88/Circular-031-esp-anexo-vf.pdf?CVID=pP5vUHj&MOD=AJPERES
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 3
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
AI in field operations: 33 of 196 projects concern production
Illustrative schematic, not a company architecture. Project counts by primary department; refining, trading and workforce projects are not shown.
Open the interactive report and every original source
03 / 8 OCT 2026
Subsurface
20
projects
Interpret rock and recommend reservoir actions.
Examples: ExxonMobil Trinidad & Tobago (with SLB) · ONGC
AI-069 · AI-225
Drilling
22
projects
Guide the well and monitor live rig data.
Examples: ExxonMobil (Guyana) · ADNOC (with SLB)
AI-072 · AI-226
Production
33
projects
Adjust artificial lift and review flow exceptions.
Examples: Devon · Chord · ExxonMobil
AI-006 · AI-097 · AI-235
Maintenance
25
projects
Identify equipment risk and choose a response.
Examples: Woodside · Equinor
AI-042 · AI-033
Safety & emissions
18
projects
Detect hazards, flare issues and operating anomalies.
Examples: Devon · Diamondback
AI-249 · AI-250 · AI-251
Business work
53
projects
Validate records, procurement and commercial decisions.
Examples: Continental · SLB · EQT
AI-248 · AI-234 · AI-095
Notes: [Sources]
- Project register by department - https://energy-ai-observatory-raj.rmistry.chatgpt.site/?exhibit=oilfield#opportunities
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 4
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
14 priority operators: 48 adoption profiles across ten departments
The cohort has 51 profiles; 3 in other departments are not shown. Shading uses the separate 20-profile deployment review. Counts describe public disclosure, not leadership or performance.
Open the interactive report and every original source
04 / 8 OCT 2026
Company | Explore | Reservoir | Drill | Produce | Maintain | HSE | Supply | Legal | Finance | IT / data
EQT |  |  |  |  |  | 1 | 1 |  |  | 
Continental Resources |  |  | 1 |  |  |  |  |  |  | 
Chord Energy |  |  |  | 1 |  |  |  |  |  | 
Devon Energy |  |  | 1 | 1 |  | 2 |  | 1 |  | 
Diamondback Energy |  |  |  | 1 |  | 1 |  |  |  | 
ConocoPhillips |  |  |  | 1 |  |  |  |  |  | 
ExxonMobil | 1 |  | 1 | 3 |  |  | 1 |  |  | 
Expand Energy |  |  | 1 | 1 |  |  |  |  |  | 
Chevron | 2 | 1 |  | 1 |  | 1 | 1 |  |  | 2
Shell |  |  |  |  | 1 | 2 |  |  |  | 1
bp |  |  | 1 |  |  | 2 |  |  |  | 
Equinor | 1 | 1 |  |  | 3 |  |  |  |  | 
Aramco | 1 |  | 1 |  |  |  |  |  | 1 | 1
ADNOC |  |  | 1 | 2 |  |  |  |  |  | 1
Includes a reviewed operating / scaled project
Reviewed pilot
Unassessed or not yet reviewed (plain)
Notes: [Sources]
- Research register and reviewed deployment subset - https://energy-ai-observatory-raj.rmistry.chatgpt.site/?exhibit=companies#opportunities
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 5
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
McKinsey’s largest modeled pools — ESP ($20bn) and drilling ROP ($16bn) — have only 1–2 matching company projects
McKinsey Exhibit 2: modeled global annual value, US$ billions. Full potential includes the near-term value; do not add the two series. Exploration ($35bn) uses a reserve-value basis and is excluded.
Open the interactive report and every original source
05 / 8 OCT 2026
Chart: 
Company projects matched
Workflow | Projects
ESP | 1
ROP | 2
Gas-lift | 6
Waterflood | 1
Predictive maint. | 7
Rod pump | 2
Schedule | 1
Supply chain | 2
Geosteering | 1
Direct matches only; one project can match several workflows. Project activity does not validate the modeled value.
Notes: [Sources]
- McKinsey · AI’s $230 billion upstream pay zone, Exhibit 2 - https://www.mckinsey.com/industries/oil-and-gas/our-insights/can-upstream-oil-and-gas-produce-value-from-ais-230-billion-dollar-pay-zone
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 6
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
Devon scaled autonomous lift from 200 wells in March to 1,000 by August 2026 — its only uplift figure (2–3%) is from the 2025 pilot
Three Devon earnings-call disclosures. The March count was recalled in August; the pilot uplift was reported in May. These sources do not provide a fleet-level production or cash result.
Open the interactive report and every original source
06 / 8 OCT 2026
2026-02-18
PILOT / ROLLOUT
Moving beyond pilots
Management links 2H-2025 lift trials to a broader 2026 rollout. No fleet result is quantified.
Original disclosure (earnings call transcript)
2026-05-06
SCALED
>850 wells live
Management reports a 2–3% production uplift from the earlier 2025 gas-lift pilot. That range does not measure the live fleet.
Original disclosure (earnings call transcript)
2026-08-05
SCALED
1,000 wells live
Real-time autonomous lift optimization now includes the first legacy Coterra wells; 2,000+ more wells are prospective.
Original disclosure (earnings call transcript)
Read-across for diligence: ask Devon-style adopters for a fleet-level comparison (treated vs. untreated wells, same period) — the pilot uplift cannot simply be multiplied by 1,000 wells.
Notes: [Sources]
- Devon Energy earnings call, 2026-02-18 - https://s2.q4cdn.com/462548525/files/doc_financials/quarterly/2025/q4/Q4-2025-DVN-Q-A-Webcast-Commentary-Transcript.pdf
- Devon Energy earnings call, 2026-05-06 - https://s2.q4cdn.com/462548525/files/doc_financials/quarterly/2026/q1/Q1-2026-DVN-Q-A-Webcast-Commentary-Transcript.pdf
- Devon Energy earnings call, 2026-08-05 - https://s2.q4cdn.com/462548525/files/doc_financials/quarterly/2026/q2/Q2-2026-DVN-Q-A-Webcast-Commentary-Transcript.pdf
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 7
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
The 10 results we reviewed in depth: 6 come from vendors alone, 3 from pilots — none pairs cost with cash
Amber text = vendor-reported or vendor co-reported. Ranges are not confidence intervals; scopes and baselines differ, so no average or ranking is implied.
Open the interactive report and every original source
07 / 8 OCT 2026
Company · measure | Reported result | Who reports it | Stage | What is missing
Devon Energy Production uplift in pilot | 2–3% uplift | Operator | Pilot result | Pilot well count and baseline; no fleet result
Chord Energy Rod-pump run time | 25% longer run time | Operator | Scaled | Runtime cohort and comparison period
TotalEnergies / Microsoft Fault-cause identification | 25–45% better | Vendor · Microsoft | Unassessed | Accuracy measure, sites, scale
Encino Energy / Ambyint Annual production decline rate | −1 pp decline | Vendor · Ambyint | Unassessed | Cohort size (344 wells on platform)
Encino Energy / Ambyint Venting events | 62% fewer events | Vendor · Ambyint | Unassessed | Baseline frequency; no methane mass or cash
ConocoPhillips / OPX Ai Production versus forecast | 3–4% above forecast | Vendor · OPX Ai | Pilot | Montney pad: well count, forecast method; four months
ConocoPhillips / OPX Ai Lease operating costs | 5% lower LOE | Vendor · OPX Ai | Pilot | Montney asset: cost pool, well denominator
ADNOC / SLB Engineering effort | 30–40% less effort | ADNOC + SLB (vendor) | Unassessed | Baseline time study
ADNOC / SLB Rig oversight capacity | 2–3× rigs per engineer | ADNOC + SLB (vendor) | Unassessed | Prior load per engineer
Continental Resources / UiPath Manual validation time | 5 min per email | Vendor · UiPath | Operating | Applies only to emails needing manual checks
Notes: [Sources]
- Devon Energy · Production uplift in pilot - https://s2.q4cdn.com/462548525/files/doc_financials/quarterly/2026/q1/Q1-2026-DVN-Q-A-Webcast-Commentary-Transcript.pdf
- Chord Energy · Rod-pump run time - https://ir.chordenergy.com/2026-02-25-Chord-Energy-Reports-Fourth-Quarter-and-Full-Year-2025-Financial-and-Operating-Results,-Issues-2026-Outlook-and-Declares-Base-Dividend
- TotalEnergies / Microsoft · Fault-cause identification - https://www.microsoft.com/en/customers/story/25505-totalenergies-agents
- Encino Energy / Ambyint · Annual production decline rate - https://www.ambyint.com/case-studies/enhancing-efficiency-and-sustainability-ambyints-infinitypl-drives-measurable-gains-for-encino-energy
- Encino Energy / Ambyint · Venting events - https://www.ambyint.com/case-studies/enhancing-efficiency-and-sustainability-ambyints-infinitypl-drives-measurable-gains-for-encino-energy
- ConocoPhillips / OPX Ai · Production versus forecast - https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
- ConocoPhillips / OPX Ai · Lease operating costs - https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
- ADNOC / SLB · Engineering effort - https://adnoc.ae/en/news-and-media/press-releases/2026/adnoc-and-slb-deploy-ai-platform-across-over-120-drilling-rigs-to-strengthen-upstream-performance
- ADNOC / SLB · Rig oversight capacity - https://adnoc.ae/en/news-and-media/press-releases/2026/adnoc-and-slb-deploy-ai-platform-across-over-120-drilling-rigs-to-strengthen-upstream-performance
- Continental Resources / UiPath / Databricks · Manual validation time - https://www.uipath.com/resources/automation-case-studies/continental-resources-streamlines-operations-with-automation
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 8
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
Four data-platform stories, no AI-only cash result — three rest on the vendor’s own case study
A data foundation (cloud, warehouse, automation) and an AI workflow are separate claims; the first does not prove the second pays.
Open the interactive report and every original source
08 / 8 OCT 2026
Company | Platform and workflow | Who reports it | What the evidence supports
Continental Resources | Databricks + UiPath: agent-assisted validation of drilling and completion data arriving by email. | Vendor · UiPath case | ~5 minutes saved per formerly manual email (not per all 200+ daily emails). No cash ROI.
Expand Energy | Snowflake / Snowpark / Cortex: forecasts, drilling analytics, SCADA site alerts. | Vendor · Snowflake case (operator release confirms relationship) | Vendor estimate of 1,000+ labor hours a year in one unit; not a production uplift.
Devon Energy | Snowflake + Whitson: daily bottomhole-pressure calculations for 5,000+ wells. | Vendor · Snowflake case | Physics workflow in use; AI attribution not established. A $50,000 sensor comparison is not realized savings.
EQT | Context Labs: production and emissions data integration. | Operator · ESG report (AI described by vendor) | Integration completed in 2024; no named AI model, price premium or emissions reduction.
Notes: [Sources]
- Continental Resources · Databricks + UiPath - https://www.uipath.com/resources/automation-case-studies/continental-resources-streamlines-operations-with-automation
- Expand Energy · Snowflake / Snowpark / Cortex - https://www.snowflake.com/en/customers/all-customers/case-study/expand-energy/
- Devon Energy · Snowflake + Whitson - https://www.snowflake.com/en/customers/all-customers/case-study/devon-energy/
- EQT · Context Labs DaaS / emissions data framework - https://esg.eqt.com/content/EQT-2024-ESG-Report.pdf
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 9
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
An ESP model missed 9 of 18 test failures. The client then approved deployment.
Baker Hughes, SPE-221571-MS (October 2024; vendor-authored; operator unnamed; three Americas assets, 137 ESPs). Pre-deployment retrospective test on 18 held-out failures; the client then approved deployment.
Open the interactive report and every original source
09 / 8 OCT 2026
Chart: 
9 of 18
held-out pump failures were missed in pre-deployment testing
Five of the nine were short circuits. Ten-minute telemetry and missing sensor data limited what the model could see.
The paper also reports successful interventions (scale and grounding caught early). Misses and deployment coexisted — the vendor published both.
One vendor study, not an industry failure rate. Metrics use different denominators (failures vs. healthy pumps).
Technical paper SPE-221571-MS · pp. 4–7
Notes: [Sources]
- SPE-221571-MS, pp. 4–7 - https://dam.bakerhughes.com/asset/2145a967-01f1-4ffa-8ee1-37b085e6fff1/spe-221571-ms-bkr-licensed.pdf
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 10
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
No operator AI cancellation was verified in this review.
5 October: 34 searches across 13 paths. The 6 October follow-up found Devon paused further video-AI development to prioritize other work. This is not a verified failed deployment or cancellation.
Open the interactive report and every original source
10 / 8 OCT 2026
0
verified operator AI
cancellations in this review
27%
say emerging tech delivers;
EY oil, gas & chemicals, n=508
85%
cite difficulty scaling successful pilots (EY, 2025)
Vendor contracts were renewed, not ended: C3 AI–Baker Hughes through June 2028; C3 AI–Shell extended June 2026.
Case | What happened | How to read it
Equinor · Havtil order · 19 Dec 2025 | Novos rollout expanded before qualification was demonstrated. Havtil ordered qualification before further rollout (deadline 1 June 2026). | Automation order; the regulator does not label Novos AI or report a malfunction.
Vår Energi · Havtil audit · 5 Feb 2026 | Automation qualification (regulator order): three non-conformities in how automated drilling is risk-assessed and qualified. | Not described as AI. Criteria must exist before systems are used.
SLB · Microsoft case · Aug 2025 | Unreadable shipping documents go to a person, a new template or retraining. | An exception step inside a vendor success story; no exception rate.
Oxy · SPE webinar · Oct 2025 | Phase two of a construction-safety vision pilot hit limited site connectivity. | Phase one described as successful; no cancellation.
NORCE / UiS / Stanford · 2021 benchmark | Repeated runs of the same geosteering AI took different well paths. | Virtual benchmark, not a well; average matched human teams.
Novi Labs · July 2023 | Barrels and gallons mixed in completion data distorted a forecasting pilot. | Outside the window; data error corrected.
Rows 3–6 describe limitations, not cancellations. The current map has 158 named relationships and 2 unconfirmed leads.
Notes: [Sources]
- Havtil · Order to Equinor (automated drilling) - https://www.havtil.no/en/supervision/important-messages/2025/order-to-equinor--technology-development-and-use-of-digital-well-planning/
- Havtil · Vår Energi audit (automated drilling) - https://www.havtil.no/en/supervision/audit-reports/2026/var-energi--risk-assessment-and-qualification-of-automated-drilling-operations/
- EY Future of Energy Survey 2025 (n=508) - https://www.ey.com/content/dam/ey-unified-site/ey-com/en-us/campaigns/energy-resources/documents/ey-ogc-future-of-energy-external-report.pdf
- SLB · Some shipping documents still needed a person - https://learn.microsoft.com/en-us/power-platform/guidance/case-studies/slb-enhances-productivity
- Oxy · Remote-site connectivity became a pilot question - https://connect.spe.org/rdts/events/eventdescription?CalendarEventKey=02eb6208-5245-4fbf-87c3-0199eb34b84c&CommunityKey=a0c6b65c-a27b-496c-8e07-9eb5cbfcea2c
- NORCE / UiS / Stanford · Repeated geosteering runs produced different paths - https://www.norceresearch.no/en/news/ai-vs-human-decision-making
- Novi Labs · customer unnamed · A unit mismatch distorted a forecasting pilot - https://novilabs.com/blog/11-costly-mistakes-ep-operators-make-in-building-machine-learning-capabilities/
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 11
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
Choose the workflow for the asset. Establish the baseline and the economics.
Practical questions for an operator or investor, drawn from the reviewed deployments and their limits.
Open the interactive report and every original source
11 / 8 OCT 2026
Operator playbook
1
Check whether the workflow fits the asset.
Devon, ExxonMobil and Chord describe fleet deployment of lift controls. Their lift types, asset conditions and measured outcomes differ.
2
Set the baseline and a control group before the pilot.
Keep untreated comparison wells after scale-up, so the fleet has a result — not just the pilot.
3
Qualify the system and fix the data.
Ten-minute telemetry and sensor gaps limited the ESP model; a barrel/gallon mix-up distorted a forecast. Norway’s regulator required qualification before further automation rollout.
Investor diligence checklist
Who reports the number?
Operator filing or call vs. vendor case study or partner release.
Pilot or fleet?
The denominator in the result cohort: wells, rigs, assets, users.
Against what?
Baseline, comparison group and measurement period.
At what cost?
All-in cost and cash conversion. Ecopetrol reports portfolio benefits, not project payback.
What failed?
Missed alerts, exception rates, and any projects stopped.
Notes: [Sources]
- Energy AI Observatory evidence synthesis - https://energy-ai-observatory-raj.rmistry.chatgpt.site/#summary
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]

## Slide 12
ENERGY AI OBSERVATORY / AI IN GLOBAL OIL & GAS, OCT 2024 – OCT 2026
Sources: every figure links to its original publication
Click any line to open the original. Speaker notes on each slide list that slide’s sources; the interactive site holds the full register and dossiers.
Open the interactive report and every original source
12 / 8 OCT 2026
Ecopetrol 2025 sustainability annex (Circular 031), p.209
www.ecopetrol.com.co
Devon Energy · Moving beyond pilots
s2.q4cdn.com
Devon Energy · More than 850 wells live
s2.q4cdn.com
Devon Energy · 1,000 wells live
s2.q4cdn.com
Chord Energy · About 99% of rod-lift wells
ir.chordenergy.com
Chord Energy · Artificial-lift optimization continues
ir.chordenergy.com
ExxonMobil · More than 1,300 Permian wells
jpt.spe.org
ExxonMobil · AI monitors production bottlenecks
corporate.exxonmobil.com
McKinsey · AI’s $230 billion upstream pay zone, Exhibit 2
www.mckinsey.com
Chord Energy · Rod-pump run time
ir.chordenergy.com
TotalEnergies / Microsoft · Fault-cause identification
www.microsoft.com
Encino Energy / Ambyint · Annual production decline rate
www.ambyint.com
ConocoPhillips / OPX Ai · Production versus forecast
jpt.spe.org
ADNOC / SLB · Engineering effort
adnoc.ae
Continental Resources / UiPath / Databricks · Manual validation time
www.uipath.com
Expand Energy · Snowflake / Snowpark / Cortex
www.snowflake.com
Devon Energy · Snowflake + Whitson
www.snowflake.com
EQT · Context Labs DaaS / emissions data framework
esg.eqt.com
SPE-221571-MS, pp. 4–7
dam.bakerhughes.com
Havtil · Order to Equinor (automated drilling)
www.havtil.no
Havtil · Vår Energi audit (automated drilling)
www.havtil.no
EY Future of Energy Survey 2025 (n=508)
www.ey.com
SLB · Some shipping documents still needed a person
learn.microsoft.com
Oxy · Remote-site connectivity became a pilot question
connect.spe.org
NORCE / UiS / Stanford · Repeated geosteering runs produced different paths
www.norceresearch.no
Novi Labs · Unit mismatch in an anonymous forecasting pilot (2023)
novilabs.com
Notes: [Sources]
[/Sources]
Revision 8 October 2026: counts use Record_type=company_adoption. Outcome_counted excludes overlapping AI-033 and AI-038 portfolio totals. Ecopetrol: 2025 AI portfolio investment and financial benefits, not complete project cost and collected cash. B means other primary publication; source authorship is shown separately. Failed-project search is bounded to this review. Current McKinsey crosswalk covers all 283 profiles. AI-180 is workflow-classified under Maintenance & reliability from its predictive-maintenance purpose; this is an analyst assignment, and IndianOil does not identify the organizational owner or buyer.
Historical 6 October follow-up: AI-086 compressor result is not explicitly AI-attributed. Devon temporarily paused further video-AI development to prioritize other AI work; restart date unconfirmed. AI-201/202 integration duration and missing full costs are clarified. The earlier follow-up left Shell/Databricks as a lead. A second 6 October source review added AI-276–279 and strengthened AI-054, 088, 089, 092, 094 and 171. Quantum operators remain unnamed; PRIO has historical-origin use; Kiewit is a yard pilot; CNRL denominators are incomplete. TC Energy capital avoidance is a forecast, and chronology is unknown. See the current register and oct6-gap-review.json for sources and decisions.
[Sources]
https://www.aogr.com/magazine/cover-story/devon-energy-stays-ahead-of-technology-curve
https://jpt.spe.org/case-study-field-deployments-of-ai-based-iocaas-advancing-artificial-lift-and-flow-assurance
https://energy-ai-observatory-raj.rmistry.chatgpt.site/?research=gaps#research
[/Sources]